## Slide 1: PlatformIO
Microcontroller Development with a Proper IDE

## Slide 2: What will we do today?
Install PlatformIO
Introduction to Microcontroller Development
Common Microcontrollers
Introduction to PlatformIO
Create a first demo project (LED blinking)
Work with the library manager
Create a more advanced Project (MQTT Messaging)

## Slide 3: Installation
Installing PlatformIO is easy, but takes some time
1
Navigate to: https://platformio.org/platformio-ide
2
Choose your IDE
3
Follow the Instructions
4
Get a coffee
5
Done

## Slide 4: Microcontroller Development
Arduino made microcontrollers popular, but more powerful options exists nowadays.
Made Microcontroller development popular
Easy to use hardware
Arduino IDE as Software option
Arduino
Started as WiFi shield for Arduinos
Great brother: ESP32
80 MHz
10-bit ADC
ESP8266
Single Board Computer
Runs full blown Linux
NOT a Microcontroller!
Raspberry Pi

## Slide 5: Microcontroller Development
Microcontroller development requires an iterative approach to hard- and software development.

## Slide 6: Microcontroller Development
Arduino programs are split into a one-time „setup“ and a recurring „loop“ function
1. Include Arduino.h (Development Framework)
3. „loop()“ defines a function which is executed in a never ending loop while the microcontroller is powered.
2. „setup()“ defines a function which is executed once at every start of the microcontroller
#include <Arduino.h>
void setup() {
Serial.begin(1200);
}
void loop() {
Serial.println("test");
delay(2000);
}

## Slide 7: Microcontroller Development
 | Used for | Syntax | Note | Size
integer | Total numbers | int var = 5; | Integers are signed by default and can overflow: When they reach their maximum value and get increased, they can „flip over“ to their minimum value. | 8-bit
float | Decimal numbers | float var = 5.5; | If doing math with floats, you need to add a decimal point, otherwise it will be treated as an int. | 32 bit
char | Single characters | char var = ‚a‘; |  | 8-bit
string | Text | string var = „text“; | Char-array can be an alternative! | As much as needed
Using c++ as development language, several data types can be used
Source: https://www.arduino.cc/reference/en/language/variables/data-types/

## Slide 8: Microcontroller Development
If – then – else | Switch
Can be used with any data type that supports logical comparison | Can be used only with int and char
if(a > 0) { Serial.println(“a is positive”); } else if(a < 0) { Serial.println(“a is negative ”); } Else { Serial.println(“a is zero ”); } | switch (someChar) { case 'a': actionOnA; break; case 'x': actionOnX; break; case 'y': case 'z': actionOnYandZ; break; default: actionOnNoMatch; }
Logically, the program can be controlled with if-then-else or switch

## Slide 9: Microcontroller Development
For | While
Executes codes and manipulates a counting variable | Executes code as long as the condition is true
for (int i = 0; i <= 255; i++) { // do something 256 times delay(10); } | while (var < 200) { // do something repetitive 200 times var++; }
For and while loops can be used to iteratively execute program parts
Source: https://www.arduino.cc/reference/en/language/structure/control-structure/

## Slide 10: Microcontroller Development
void loop () {
int i = test();
Serial.println(i);
}
int test () {
return 1;
}
Functions can be used for logical seperations of program parts

## Slide 11: What is PlatformIO?
Extension for many regular IDEs
Replacement of the Arduino IDE
Library Manager
Code Manager
Toolchain
PlatformIO integrates microcontroller development into existing IDEs
Notes: Folie einbauen Vorstellung ESP8266 & Mehr basics zum Thema DIE (ggf. Bilder zum Thema Microcontroller Programmierung)

## Slide 12: Why PlatformIO?
Arduino IDE sucks!
Support for over 200 boards and platforms
Integrated in your favorite IDE
Automated toolchain installation
Library Manager! (Including Updates!)

## Slide 13: First Project - Start
PIO Home  New Project
Project Wizard
  Name your project
  Select your board (You can search)
  Select the Framework
  Select the Location (or keep default)
Grab a coffee
Switch back to your workspace
Open src  main.cpp
Creating a new project with PlatformIO is easy due to the offered wizard

## Slide 14: First Project – Code
Include Arduino.h
In your setup():
  Define LED_BUILTIN as output
In your loop:
  Turn LED_BUILTIN low
  Wait 1 second
  Turn LED_Builtin High
  Wait 1 second
/*
* Blink
* Turns on an LED on for one second,
* then off for one second, repeatedly.
*/
#include <Arduino.h>
void setup()
{
// initialize LED digital pin as an output.
pinMode(LED_BUILTIN, OUTPUT);
}
void loop()
{
// turn the LED on (HIGH is the voltage level)
digitalWrite(LED_BUILTIN, HIGH);
// wait for a second
delay(1000);
// turn the LED off by making the voltage LOW
digitalWrite(LED_BUILTIN, LOW);
// wait for a second
delay(1000);
}

## Slide 15: First Project – platformio.ini
Contains your project settings
Autogenerated, but can be adjusted
Important addtions:
  upload_port
    Specifies the port to upload the code to
    Can be a COM port (for serial uploads)
    Can be a hostname (OTA updates)
  monitor_port
    Specifies the serial port to monitor
    For debugging
  lib_deps
    Tells the IDE, which libraries are needed
[env:esp32doit-devkit-v1]
platform = espressif32
board = esp32doit-devkit-v1
framework = arduino
upload_port = COM5
monitor_port = COM5
lib_deps =
ArduinoJson

## Slide 16: First Project – Build and Run
Use the Toolbar:
Or: Use the PIO Button (See right)
Build (and check the results)
Upload to the board
Enjoy a blinking LED (or start debugging)

## Slide 17: Library Manager - Install
PIO Home  Libraries
Search, Install and Update libraries
Example: Search for „PubSubClient“
  This is the most reliable MQTT Implementation
Click on the library
Hit „Install“
Check the examples!

## Slide 18: Library Manager – Install via git
Sometimes a library is not in the manager
Sometimes you need a fork
Example: VS1053 Fork for the ESP
  https://github.com/danclarke/Adafruit_VS1053_Library
Go to the Library Manager
Click „install“ (without searching)
Enter the URL for the git repo
Note: This puts the library into .piolibdeps
  NOT shared on git!

## Slide 19: Library Manager – Installed Libs
Get an overview on installed libraries
Access examples
Global Storage & Project Storage

## Slide 20: Library Manager – Update Libs
Automatic detection of updates
Update library with 1 click

## Slide 21: Next Project – MQTT Messaging
MQTT is a lightweight messaging protocol
Central Broker (server) handles messages
Clients:
  Subscribers can subscribe to topics
  Publishers can publish messages to topics
Used widely in IoT applications

## Slide 22: MQTT Project – Structure
Based on the Example from the library!
Connect to the WiFi
Setup:
  Connect to the MQTT Server
  Subscribe to your topics
Loop:
  Handle messages: client.loop();
  Publish something
WiFi SSID: „CoMakingSpace“
Password: just ask ;)
mqtt_server = "comakingcontroller"
Notes: Folien einbauen zum debuggen via Serial Port

## Slide 23
Thank you!
Notes: Aufgaben einbauen zur Interaktion mit Sensoren / der echten Welt

## Slide 24: Stay in Touch
www.comakingspace.org
wiki.comakingspace.org
github.com/comakingspace

## Slide 25: Stay in Touch
Like us on Facebook
facebook.com/comakingspace
Follow us on Twitter
@comakingspace
Follow us on Instagramm
instagram.com/comakingspace/
Sign up for our newsletter:
https://lists.schokokeks.org/mailman/listinfo.cgi/comaking-news
Join the Heidelberg Makers WhatsApp Group
⚙Maker Community HD⚙
https://chat.whatsapp.com/AXuJcYqno64CUjsWsEmma4
Check Our WebSite
www.comakingspace.org
Get informed on our Wiki
wiki.comakingspace.org
Help with coding and other issues
Github.com/comakingspace

## Slide 26: Preperation – Platform Installation
PIO Home should have opened automatically
  If not, reload your IDE or press:
Switch to „boards“
Search for your board (e.g „Devkit V1“)

## Slide 27: Preperation – Platform Installation
Click on the platform name
Hit „Install“

## Slide 28: Preperation – Platform Installation
Check the examples to get familiar with your platform:

## Slide 29: Microcontroller Development
Data type
What is it?
int var = val;
Integers are signed by default and can overflow: when they reach their maximum value and get increased, they can „flip over“ to their minimum value.
Integers are your primary data-type for number storage
Integer
Syntax
Note

## Slide 30: Microcontroller Development
Primary data-type for storing total numbers
Integer
int var = 5;
Syntax
Integers are signed by default and can overflow: when they reach their maximum value and get increased, they can „flip over“ to their minimum value.
Note
Primary data-type for storing decimal numbers
Float
float var = 5.5;
Syntax
If doing math with floats, you need to add a decimal point, otherwise it will be treated as an int.
Note
Primary data-type for storing characters
Char
char var = ‚a‘;
Syntax
-
Note
Primary data-type for storing text
String
string var = „text“;
Syntax
Char-array can be an alternative!
Note

## Slide 31: Microcontroller Development
Integer | Float | Char | String
Storing total Numbers | Storing decimal numbers | Storing ASCII characters | Storing text
int var = 5; | float var = 5.5; | char var = 'a'; | string var = "text";
Integers are signed by default and can overflow: when they reach their maximum value and get increased, they can „flip over“ to their minimum value. | If doing math with floats, you need to add a decimal point, otherwise it will be treated as an int. |  | Char-array can be an alternative!